## Slide 1: Remote Network Server Access
Michael P. Andrews
Ameritech Electronic Commerce
Senior Technology Consultant
Network Services - National Operations
Mike.Andrews@Ameritech.COM
Mike@MikeA.COM

## Slide 2
Work At Home
Intranet Access
On-Line Access

## Slide 3: Introduction
Need to provide services on the Corporate LAN and/or Intranet to remote users:
  I/T support staff
  “Road Warriors”
  Other staff working from home
  Contractors and vendor support staff

## Slide 4: Introduction
Today’s Applications require live, “real time” access:
  Email
  Web
  Database

## Slide 5: Summary
How to provide transparent remote access to all services on multiprotocol LAN servers
How to maximize performance
How to maintain security
Configure Windows 95 / NT 4.0 client
Configure Access Server / Router

## Slide 6: Summary (cont.)
Protocols
  TCP/IP
    Internet / Intranet
    Microsoft NT
  IPX
    Novell NetWare / IntraNetWare
    Microsoft NT
  NETBEUI (NETBIOS)
    Windows for Workgroups
    Windows 95
    Microsoft NT

## Slide 7: What remote access are you using now?
What types of servers do you have?
  Are you using or planning on using NT?
What kind of remote users?
  How easy for users to dial in?
  How usable is the access speed?
What kind of security is in place?
  Firewall
  Token authentication
  VPN

## Slide 8: Agenda
a little Theory on Communications technology
Security methods
Network planning
Windows 95 configuration
(General) Access server configuration

## Slide 9: Up and Down the stack
The Network Layers (again???)
  Application
  Presentation/Session
  Transport
  Network
  Data Link
  Physical

## Slide 10: TCP/IP on LAN
The Network Layers
  Netscape (Application)
  HTTP (Presentation/Session)
  TCP (Transport)
  IP (Network)
  Ethernet (Data Link)
  Twisted Pair (Physical)

## Slide 11: TCP/IP on Dial-up
The Network Layers
  Netscape (Application)
  HTTP (Presentation/Session)
  TCP (Transport)
  IP (Network)
  PPP (Data Link)
  Serial Modem (Physical)

## Slide 12: Application “doesn’t see a difference”
LAN
  Netscape
  HTTP
  TCP
  IP
  Ethernet
  Twisted Pair
Dial-up
  Netscape
  HTTP
  TCP
  IP
  PPP
  Serial Modem

## Slide 13: SLIP vs. PPP
SLIP
  Serial Link IP
  IP with minimal header
  No error checking
  IP ONLY
PPP
  Point to Protocol
  HDLC
  LCP - Error checking
    LQM - FCS
  NCP - Carries Multiple Protocols:
    IPCP (IP)
    IPXCP (IPX)
    ATCP (Appletalk)
    NBCP (NetBIOS)
Notes: SLIP header - END Decimal 192
ESC - Decimal 219
Replaces data END with ESC-Dec 220
Replaces data ESC with ESC-Dec 335
Sends IP datagram followed by END
HDLC- High Level Data Link Control, ISO - 3309 also used in X.25, Frame Relay, and ISDN.
LCP - Link Control Protocol
FCS - Frame Check Sequence -16-bitCRC
Link Quality Monitoring - Definable test of link failure
NCP - Network Control Protocols
LCP and NCP negotiate Network Layer connection between the two points

## Slide 14: PPP Node Authentication
PAP
  plain text password sent across line during PPP negotiation
CHAP
  password is MD5 digest key to random challenge, password never crosses the link
  challenge periodically re-occurs during PPP connect

## Slide 15: Out of Band Node Authentication
Username/Password
  Use script to answer prompts
  password may be exposed
Caller ID
  reject call if not from home number
  doesn’t support “Road Warriors”
Callback

## Slide 16: More Secure Node Authentication
One time Password
  S/Key
    software freely available
  Token
    SecureID
    others

## Slide 17: Dial-up Link choices
Analog Modem
Cellular Modem
Digital ISDN “Modem”
Digital ISDN Router
Packet Services
ADSL

## Slide 18: Analog Modem
Available in Internal/External/PC card
Uses existing POTS phone line
*67, to disable Call Waiting
Lifting phone extension causes errors
Best with separate phone line
Adapters available for use with Digital PBX lines (connects to handset)

## Slide 19: V.34bis Modem
up to 33.6Kbps
Error correcting
Adaptive link speed
  “downshifts” for poor-quality lines
Data Compression
  up to 4X better throughput

## Slide 20: 56Kbps Modem
Same features but…
Requires Digital lines at POP (more later)
Two incompatible “standards”
  X2 (USR)
  K56Flex (Rockwell,Lucent,others)
Now limited to 52Kbps

## Slide 21: Cellular Modem
Call (modem carrier) gets interrupted as cells change
MNP 10 required
  Special interruption tolerant protocol
  Must be on modems at both ends
V.34bis modem will work (sorta)
  Set higher “carrier loss detect” S register on both sides

## Slide 22: What can ya expect?
Good performance for API, data only applications
  Web
  File transfer
  SMTP, POP, or API E-mail

## Slide 23: What d’ya expect?
Lousy perfomance for DOS file access intensive applications
  Running apps from file server
  DOS Database apps
  Microsoft Mail 3.2
Disable processing of Novell server logon scripts

## Slide 24: Use remote control for those
Remote Control Products that use TCP/IP or IPX network transport will work OK
  Symantec PC Anywhere 32
  Carbon Copy
  Stac Reachout Remote

## Slide 25
ISDN
It Still Does Nothing*

## Slide 26
ISDN
It Still Does Nothing*
*if you don’t try it

## Slide 27
How Does ISDN Work?
ISDN provides a standard “pipe” called the Basic Rate Interface.
BRI is transmitted over the normal 2-wire copper cable facilities which are familiar to telephone transmission all over the world.
Unlike ordinary analog transmission which restricts this pipe to one conversation at a time, BRI combines, or multiplexes, three communications channels into that one pipe - all of which can be used simultaneously.

## Slide 28
Basic Rate Interface (BRI)
Two B Channels
B Channels - User, Voice, Data, Image, Sound
D Channels - Call Signaling, Set-up, User Packet Data
One BRI = 2B + D
16 Kbps D Channel

## Slide 29: A 64Kbps “line”
Also called “DS0”
Standard digital US phone call unit
Supports one Voice call
8 bits sampled @ 8,000 times/second
  =64,000 bits per second
  =64Kbps
Faster lines are time-div-multiplexed groups of DS0s

## Slide 30: ISDN BRI features
Special Digital Line delivered on a single pair
BRI - Two 64Kbps B Channels
Call sets up in seconds
Use spare B for
  Voice
  FAX
  Analog Modem (some have built-in)
Combine B’s for 128Kbps with
  BONDING (no “demand” to it!)
  MPPP (Multilink PPP)

## Slide 31: ISDN “Modem”
Not really a “Modem” - ISDN TA
Internal / External / PC card
External has serial port connection to PC
  serial bottleneck causes less than optimum performance (more later)
Some have Parallel port
Data Compression
  up to 4X better throughput (200-300Kbps)

## Slide 32: ISDN Router
External with 10Mbps Ethernet (10BaseT) port
PC requires LAN card
Some with BOOTP/DHCP to dynamically assign IP address
Data Compression
  up to 4X better throughput (200-300Kbps)

## Slide 33: What does ISDN cost?
Residential BRI
  Install ~$150
  Monthly ~$34.00
  Each B usage charge same as POTS phone line
    “A Band” (8 miles) “Nickel zone” call .05 untimed
    “B Band,” “C Band” calls timed

## Slide 34: How to order ISDN
Call 1-800-TEAM-DATA (Business orders from CBS, EBS, or SBS. See phone bill)
Order National ISDN1
Switched Voice/Data on BOTH B channels
Phone numbers on BOTH B channels
Indicate equipment vendor
ISDN Provisioning center will FAX order confirmation with SPIDs

## Slide 35: Choosing ISDN equipment
Choose built-in NT (Network Terminator)
Look for unit with one or two POTS jacks for analog phone and FAX
Look for EZ setup

## Slide 36: Configuring ISDN device
Switch type: National ISDN1
Enter SPIDs, LDN (phone numbers)
  LDN1: 8479361212
  SPID1: 84793612120111
  LDN2: 8479361213
  SPID2: 84793612130111

## Slide 37: Serial is a Killer
ASYNCH port ships 10 bits for 8-bit byte of data, a 20% overhead
38,400bps, 57,600bps, 115,200bps (not as fast as raw 128Kbps 2B ISDN!)
Requires 16550 or 16650 UART with FIFO buffer
PC / Windows cannot service serial port interrupts fast enough, losing data
Lowering the port speed may improve throughput performance! (check PPP stats)

## Slide 38: Network Protocols

## Slide 39: Network Protocols
TCP/IP
IPX/SPX
NetBEUI (NetBIOS)

## Slide 40: TCP/IP
Universal DOD protocol of the Internet
Requires unique network address (or NAT)
Routable - choice of routing protocols, typically RIP
Scalable packet size
Commonly used to carry (tunnel) other protocols like IPX, NetBEUI, SNA

## Slide 41: Remote TCP/IP Network Planning
Either
Hard code Client IP address
  For node identification, DNS rev, Security
  or
Assign IP addresses during PPP negotiation
  Server has IP address pool

## Slide 42: Remote TCP/IP Network Planning
Either
Treat remote nodes as separate advertised subnet
  or
Use existing subnet with proxy ARP
Same DNS, WWW, Email, etc. server addresses

## Slide 43: Remote TCP/IP Network Planning
Same DNS, WWW, Email, etc. server IP addresses

## Slide 44: VPN - Secure TCP/IP
The Network Layers
  Netscape (Application)
  HTTP (Presentation/Session)
  TCP (Transport)
  IP (Network)
  ENCRYPTION
  PPP (Data Link)
  Serial Modem (Physical)

## Slide 45: VPN - Secure TCP/IP
Secure link from node to firewall, even across unsecure networks, i.e.. the Internet
IPSec
  part of IETF IPv6 (but v6 not required)
  Triple DES encryption
  even IP address encrypted

## Slide 46: IPX / SPX
Novell Netware / IntraNetWare
Typical 128Kbyte (small) packet size
Primarily File or Print services
Broadcast to locate servers
SAP service broadcasts
RIP routing updates

## Slide 47: Remote IPX Network Planning
New arbitrary IPX network
IPX network-node address during PPP negotiation
  Server has IPX network address for remote nodes
  Remote client generates node address
Use outbound SAP filters (unless server is remote)

## Slide 48: NetBEUI Net BOO! Hiss!
Extension of NetBIOS
  Developed by IBM as basic LAN protocol
  Emulates BIOS file access
  Later by Microsoft LAN Manager
Everything is a broadcast
Not routable
Used by WFW, Win95, NT Network chooser

## Slide 49: NetBEUI Network Planning
Need it to make access friendly
Best to tunnel it!
NetBEUI<--->WINS <---> TCP/IP <---> WINS <--->NetBEUI
NetBEUI <---> IPX <---> NetBEUI
Or use NBCP in PPP link (like RAS server)
Or… use local LMHOSTS file

## Slide 50: On the client side

## Slide 51: Windows 3.1, 3.11 (Windows for Workgroups)
Recommend Stampede Remote Office Gold
  www.stampede.com

## Slide 52: Windows 95/NT
“Dial-up” networking
  In Control Panel or Accessories
  Install from CD as “Communications”
Primary logon --> Windows logon
Enter node “username”, password. Click on “Save password”

## Slide 53: Resist the urge to tinker!
Microsoft talks funny. Some options have strange behavior. The defaults are usually correct!

## Slide 54: On the server side

## Slide 55
Primary Rate Interface (PRI)
One PRI =
United States: 23 B+D
Europe/Asia: 30/31 B+D
B Channels -
User Voice, Data
Image, Sound
D Channels -
Call Signaling,
Set-up, User
Packet Data
23 B Channels
64 Kbps D Channel

## Slide 56: PRI, the Hot Setup
23 channels (lines) serve both analog modem and digital ISDN users
Digital “further in” gives clearer line
D channel indicates voice call ---> software modem “emulator”
D channel indicates digital call ---> digital “all the way”

## Slide 57: PRI, the Hot Setup
Supports “Caller ID” for logging, security
23 lines on one port for high density
Up to 268 lines in one 19” rack device (Bay Networks)
Setup used by large ISPs (i.e.. AOL)

## Slide 58: Resist the urge to tinker!
The defaults are usually correct!

## Slide 59: Where to get more information
Dan Kegel’s ISDN page - http://alumni.caltech.edu:80/~dank/isdn
Vendors
  www.ascend.com
  www.adtran.com
  www.baynetworks.com
  www.cisco.com
  www.microsoft.com
  www.shiva.com

## Slide 60: User database
Local
  may be limited
TFTP, DNS server
  data may be exposed
Authentication database server
  TACACS, TACAS+
    Cisco
  Radius
    others

## Slide 61: Activity logging
SYSLOG
SNMP Traps
Authentication database server
  TACACS
  Radius
Parse logs with Perl to do reports, billing

## Slide 62: Where to get more information
Usenet Newsgroups (or… use http://www.dejanews.com)
  comp.protocols.tcp-ip
  comp.protocols.ppp
  comp.dcom.isdn
  comp.dcom.modems
  comp.dcom.servers
  comp.dcom.modems

## Slide 63: Where to get more information
Network Computing Magazine http://techweb.cmp.com/nc/docs
The ISDN Literacy Book Gerald L. Hopkins, Addison-Wesley Pub. Co. ISBN#0201629798